## Slide 1: Data Representation

## Slide 2: Table of Contents
Brief Table of Contents.
Introduction
Number System
Number Conservation
Binary Arithmetic
Logic Gate

## Slide 3: Introduction
In computer systems, data refers to symbols used to represent numbers, text, events, sounds, images, people, things, ideas, etc.

## Slide 4: Number System
Number system is a basis for counting various items.
Number system is a way to represent or express numbers.
Number system refers to the digits, its arrangements, positional value and base of number system.
Types of Number System
  Non Positional Number System
  Positional Number System

## Slide 5: Positional Number System
A positional number system is one in which a number's position represents different values ​​depending on the position it occupies in the number.
Few symbols are used and the value of each digit is determined by three considerations.
  The digit itself
  The position of digit in the number
  The base of the number system
The rightmost digit have minimum and leftmost digit have maximum positional weight.
Types of Positional Number System
Decimal Number System – (Base 10)
Binary Number System – (Base 2)
Octal Number System – (Base 8)
Hexadecimal Number System – (Base 16)

## Slide 6: Decimal Number System
Characteristics of decimal number system
Uses ten digits 0, 1, 2, 3, 4, 5, 6, 7, 8 and 9
Redix(r) = 10
Example
A number system having base 10 is called decimal number system.
Decimal number system is very popular in our day-to-day life.

## Slide 7: Binary Number System
Characteristics of binary number system
Uses two digits 0 and 1
Redix(r) = 2
Example
A number system having base 2 is called binary number system.
Used in computer system.

## Slide 8: Octal Number System
Characteristics of octal number system
Uses two digits 0, 1, 2, 3, 4, 5, 6 and 7
Redix(r) = 8
Example
A number system having base 8 is called octal number system.

## Slide 9: Hexadecimal Number System
Characteristics of hexadecimal number system
Uses ten digits and six letters 0, 1, 2, 3, 4, 5, 6, 7, 9, A, B, C, D, E and F
Redix(r) = 16
Example
A number system having base 16 is called hexadecimal number system.

## Slide 10
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 000 | 0
1 | 0001 | 001 | 1
2 | 0010 | 002 | 2
3 | 0011 | 003 | 3
4 | 0100 | 004 | 4
5 | 0101 | 005 | 5
6 | 0110 | 006 | 6
7 | 0111 | 007 | 7
8 | 1000 | 010 | 8
9 | 1001 | 011 | 9
10 | 1010 | 012 | A
11 | 1011 | 013 | B
12 | 1100 | 014 | C
13 | 1101 | 015 | D
14 | 1110 | 016 | E
15 | 1111 | 017 | F

## Slide 11: Number Conversion
Separate the number into integer and fractional part
Divide “integer part” by base r repeatedly until the quotient becomes zero and storing remainders at each step
Multiply “fractional part” by r and accumulate the integer digits so obtained
Combine the accumulated result and parenthesis, the whole result with subscript r.
Decimal to base-r system
ABC.XYZ
ABC XYZ
r ABC reminder XYZ × r i

## Slide 12: Decimal to Binary
Divide the given number by 2 and note their remainder
Repeatedly divide the quotient by 2 and note the remainder until quotient reduced 0.
Collect the remainders, last obtained first and first obtained last to get binary equivalent.
Rules
Example
2 75
37
18
9
4
2
1
0
1
1
0
1
0
0
1

## Slide 13: Decimal to Octal
Divide the given number by 8 and note their remainder
Repeatedly divide the quotient by 8 and note the remainder until quotient reduced 0.
Collect the remainders, last obtained first and first obtained last to get binary equivalent.
Rules
Example
8 75
9
1
0
3
1
1

## Slide 14: Decimal to Hexadecimal
Divide the given number by 16 and note their remainder
Repeatedly divide the quotient by 16 and note the remainder until quotient reduced 0.
Collect the remainders, last obtained first and first obtained last to get binary equivalent.
Rules
Example
16 1013
63
3
0
5
E
3

## Slide 15: Binary to Decimal
Multiply each bit by corresponding power of 2 (base)
Sum each product term to get decimal equivalent number.
Rules
Example

## Slide 16: Binary to Octal
Divide given binary number into group of three bits from binary point right.
Substitute each group of three bits by octal equivalent.
Collect octal digits to get equivalent number
Rules
Example

## Slide 17: Binary to Hexadecimal
Divide given binary number into group of four bits from binary point right.
Substitute each group of three bits by hexadecimal equivalent.
Collect octal hexadecimal to get equivalent number
Rules
Example

## Slide 18: Octal to Decimal
Multiply each octal digit by corresponding power of 8 (base)
Sum each product term to get decimal equivalent number.
Rules
Example

## Slide 19: Octal to Binary
Substitute each octal digit by equivalent 3 bit binary
Collect for each digit to get binary equivalent number
Rules
Example

## Slide 20: Hexadecimal to Decimal
Multiply each octal digit by corresponding power of 16 (base)
Sum each product term to get decimal equivalent number.
Rules
Example

## Slide 21: Hexadecimal to Binary
Substitute each hexadecimal digit by equivalent 4 bit binary
Collect for each digit to get binary equivalent number
Rules
Example

## Slide 22: Binary Arithmetic
Rules for binary addition
Binary Addition
Rules for binary subtraction
Binary Subtraction

## Slide 23: Subtraction using complement
Complement are used in the digital computer to simplify the subtraction operation and for logical manipulations. There are two types of complements in binary number system, 1’s complement and 2’s complement.
Rules
Make equal number of bits in both subtrahend and minuend
Find 1’s / 2’s complement of subtrahend
Add minuend to it
In 1’s
  If sum produce carry, add it to LSB of the sum (Ans is +ve)
  If sum doesn’t produce carry, take 1’s complement of result (Ans is -ve)
In 2’s
  If sum produce carry, discard it (Ans is +ve)
  If sum doesn’t produce carry, take 2’s complement of result (Ans is -ve)
How to find 1’s complement?
Subtract each bit from 1.
How to find 2’s complement?
Find 1’s complement and add 1 to LSB.

## Slide 24: Example
Perform 1’s complement and 2’s complement of
1’s Complement:
Since, carry is not found, so result is negative and again find its 1’s complement
2’s Complement:
Since, carry is not found, so result is negative and again find its 2’s complement

## Slide 25: Logic Gate
A logic gate is an electronic circuit that operates on one or more input signals to produce an output signal. Gates are the hardware components, which produce signals 1 or 0 if input requirements are satisfied. Types of logic gates:
AND gate
OR gate
NOT gate
NAND gate
NOR gate

## Slide 26: AND Gate
An electronic circuit have two or more than two input values and produce only one output value
Produce 1 output when all input are 1 otherwise the output will be 0
Algebraic Expression
  O = A.B
Graphical Symbol
Truth Table
Inputs |  | Outputs
A | B | O = A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 27: OR Gate
An electronic circuit have two or more than two input values and produce only one output value
Produce 0 output when all input are 0 otherwise the output will be 1
Algebraic Expression
  Y = A+B
Graphical Symbol
Truth Table
Inputs |  | Outputs
A | B | Y = A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 28: NOT Gate
An electronic circuit have only one input values and produce only one output value
Produce complement of input value
Algebraic Expression
  Y =
Graphical Symbol
Truth Table
Inputs | Outputs
A | Y =
0 | 1
1 | 0
Inputs | Outputs
A | 
0 | 1
1 | 0

## Slide 29: NAND Gate
An electronic circuit have two or more than two input values and produce only one output value
Combination of AND and NOT gate
Algebraic Expression
  Y =
Graphical Symbol
Truth Table
Inputs |  | Outputs
A | B | Y =
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Inputs |  | Outputs
A | B | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 30: NOR Gate
An electronic circuit have two or more than two input values and produce only one output value
Combination of OR and NOT gate
Algebraic Expression
  Y =
Graphical Symbol
Truth Table
Inputs |  | Outputs
A | B | Y =
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Inputs |  | Outputs
A | B | 
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 31: Thank You